## Slide 1: Rack Power Distribution
Internal Training
October 08th 2014
Thomas Hofbauer
Product Manager

## Slide 2: Competitive Product Comparison
 | MPH2 | APC 8xxx | Raritan PX2 | Servertech
Product Range | Outlet Metered & Switched; Outlet Metered; Branch Metered & Outlet Switched; Branch Metered | Outlet Metered & Switched; Branch Metered & Outlet Switched; Branch Metered | Outlet Metered & Switched; Outlet Metered; Branch Metered & Outlet Switched; Branch Metered | Outlet Metered & Switched; Outlet Metered; Branch Metered & Outlet Switched; Branch Metered
0U Cross Section | 28,4 cm2 | 28,4 cm2 | 35,5 cm2 | 39,5 cm2
Temp. Rating | 60°C | 45°C | 60°C | 40°C
Metering Accuracy | + / - 1% | + / - 3% | + / - 1% | + / - 2%
Idle Power Draw (Switched) | 5 Watts | 17.7 Watts | 20.2 Watts | ?
Controller Card | Modular, Hot swappable | Modular | Embedded | Embedded
Locking Outlets | Standard | Standard | Optional | Optional
Overcurrent Protection | Resettable Slim profile CB | Resettable Slim profile CB | Resettable CB | Resettable Slim profile CB
Power Default (Switched) | Power Delivery | Dropped Load | Dropped Load | Dropped Load
Display Options | On-board & Local Display | Local fixed | Local fixed | Local fixed
Power Array | Up to 4 | Up to 4 | Up to 4 | Up to 2
Communication Options | Web UI, CLI, SSH, Telnet, SNMP v1,2,3 | Web UI, CLI, SSH, Telnet, SNMP v1,2,3 | Web UI, CLI, SSH, Telnet, SNMP v1,2,3 | Web UI, CLI, SSH, Telnet, SNMP v1,2
Authentication Options | Local, Radius, LDAP, Active Directory, Kerberos, TACACS | Local, Radius | Local, TACACS+, Radius, LDAP | Local, Radius, LDAP, TACACS

## Slide 3: Competitive Product Comparison Rittal
 | MPH2 | Rittal
Product Range | Outlet Metered & Switched; Outlet Metered; Branch Metered & Outlet Switched; Branch Metered | Outlet Metered & Switched; Branch Metered & Outlet Switched; Branch Metered
0U Cross Section | 28,4 cm2 | 28,4 cm2
Temp. Rating | 60C | 45C
Metering Accuracy | + / - 1% | + / - 2%
Idle Power Draw (Switched) | 5 Watts | ?
Controller Card | Modular, Hot swappable | Embedded
Locking Outlets | Standard | Optional
Overcurrent Protection | Resettable Slim profile CB | Resettable CB
Power Default (Switched) | Power Delivery | Power Delivery
Display Options | On-board & Local Display | Local fixed
Power Array | Up to 4 | Up to 4
Communication Options | Web UI, CLI, SSH, Telnet, SNMP v1,2,3 | Web UI, SSH, Telnet, SNMP v1,2,3
Authentication Options | Local, Radius, LDAP, Active Directory, Kerberos, TACACS | Local, Radius, LDAP, Active Directory

## Slide 4: Competitive Positioning - APC
Value Proposition | Feature | ENP | APC
High Availability | Adaptive Offering |  | 
 | High Temp. rating | 60°C | 45°C
 | Hot Swappable Communications Module |  | 
 | Bistable / Normally closed relays |  | 
Optimized Energy & Capacity Management | Measurement Accuracy | +/- 1% | +/-3%
 | Idle Power consumption – Switched Managed units | 5W (MPH2) | > 18W
Simplified Appliance & Application Integration | Remote Authentication | LDAP, Active Directory, Radius, TACACS, Kerberos | Radius
 | Dedicated Centralized PDU Management software |  | 
Easy Physical & Electrical Integration | Ship Preinstalled in racks |  | 
 | Outlet Metered Models |  | Limited
 | Hardwired Models |  | 

## Slide 5: Competitive Positioning - Servertech
Value Proposition | Feature | ENP | Servertech
High Availability | Adaptive Offering |  | 
 | High Temp. rating | 60°C | 45°C (60°C on a few selected models only)
 | Bistable / Normally closed relays – Switched Models |  | 
 | Modular Hot Swappable Communications Card |  | 
 | Locking Outlets |  | Only on selected models
Optimized Energy & Capacity Management | Measurement Accuracy | +/- 1% | +/-2%
 | Idle Power consumption – Switched Managed units | 5W (MPH2) | > 18W
Simplified Appliance & Application Integration | # of PDU’s within a Power Array | 4 | 2
Easy Physical & Electrical Integration | 0U Managed Units – Cross sectional area | 28,4 cm2 | 39,5 cm2
 | Flexible Input Power cord entry – Managed offerings |  | Only on selected models

## Slide 6: Competitive Positioning - Raritan
Value Proposition | Feature | ENP | Raritan
High Availability | Adaptive Offering |  | 
 | Bistable / Normally closed relays – Switched Models |  | 
 | Modular Hot Swappable Communications Card |  | 
 | Locking Outlets |  | Only on selected models
Optimized Energy & Capacity Management | Idle Power consumption – Switched Managed units | 5W (MPH2) | > 18W
Easy Physical & Electrical Integration | 0U Managed Units – Cross sectional area | 28,4 cm2 | 35,5 cm2
 | Flexible Input Power cord entry – Managed offerings |  | Only on selected models

## Slide 7: Competitive Positioning - Rittal
Value Proposition | Feature | ENP | Rittal
High Availability | Redundant Communication Pat |  | optional
 | High Temp. rating | 60°C | 45°C
 | Software Electronic Overcurrent Protection |  | 
 | Modular Hot Swappable Communications Card |  | 
 | Locking Outlets |  | optional
Optimized Energy & Capacity Management | Measurement Accuracy | +/- 1% | +/-2%
 | Idle Power consumption – Switched Managed units | 5W | ?
Simplified Appliance & Application Integration | Remote Authentication | LDAP, Active Directory, Radius, TACACS, Kerberos | Radius, LDAP, Active Directory
Easy Physical & Electrical Integration | Hardwired items |  | 
 | Flexible Input Power cord entry |  |